## Slide 1
SHORT format
Display: Inner, Outer, Groove, Pitch Center, ROC
Display Cam-profile as: Profile only, Pressure-Angle, Maximum Shear Stress, Contact-Force
Edit: Color, Line Thickness,
Enable: Lifetime calculations, Enter Safety-Factor
EXTENDED format
Select Roller: Manufacturer, P/N,
Enable ISO 281 Factors: Enter Reliability and Lubrication factors
Select Cam: Steel and Heat-Treatment, Quality,
Enter: Surface Hardness
Find Roller L10, and Lnm Lifetime
Find Cam Lifetime
Click
Click
STEP 1: Configure Power Source
In the Kinematics-Tree, edit the Kinematic-chain that includes the Follower Part
Select the 2D-Cam as the Power-Source
Add Cam-Data FB
Open Cam-Data FB
Link to a 2D-Cam
Force
Shear-Stress
ROC
Pressure-Angle
Sliding-Velocity
2D-Cam
Edit 2D-Cam
Graph to:
Analyse
Export data
.STEP model of Cam-Plate: ID, OD, Thickness, …
.DXF : Profile : Lines or BiArcs
.TXT : XY Coordinates or BiArc data
Export directly to SOLIDWORKS
Open Cam-Data FB (again)
Save Cam Profile as …
Profile
YOU ARE HERE